## Slide 1
ESSE 4690 Lab 02
Course Director: Dr. Gunho Sohn
TA: Maryam Jameela
30th Sep 2021
Canny Edge Detection

## Slide 2: Submission
Code with descriptions
Result images
Report (max 10-12 pages)
  Implementation procedure (be simple)
  Result (images with titles and descriptions)
  Discussion (major part)
  No code in Report
  Submit Code, Report and Results in Separate folders and Zip them Together
Upload them via eClass: Due 08:00pm, 7th Oct, 2020
Hints: Read the Lab2 introduction in detail
or email TA via maryumja@yorku.ca if you have more questions

## Slide 3: Objectives
Implementation of Canny edge detection algorithm
Understanding of Canny edge detection theory
Optimization: Parameter tuning

## Slide 4: Why Edge Detection
Most of the shape information of an image is enclosed in edges.
To locate and extract the boundaries of objects within the image.
To spot the discontinuity of brightness.
To reduce the amount of information to be processed for image analysis.
To preserve essential structural properties of an image.

## Slide 5: Training Procedure
Image
Smoothing
Edge
Computation
Non-maximum
Suppression
Edge
Linking
Quality
Assessment
OK?
Input
No
Yes
Output
Edge Localization
Adjust
Parameters
 tl th

## Slide 6: Image Smoothing
Convolution operation over input image using gaussian kernel to produce the blurred feature map of low frequency. By blurring the image or smoothing we decrease the edge content.
Image = imread(image_path)
Image_ gray = rgb2gray(image)
Gaussian_filter = fspecial(‘gaussian’, kernel_size, sigma)
Image_smoothed = im_myfilter(image_gray, Gaussian_filter)

## Slide 7: Edge Computation
-1 0 1
Sx  -2 0 2
-1 0 1
1 2 1
Sy  0 0 0
1 2 1
Sobel:
Gx  I Sx
2
s
x
y
G 2
E 
G
o
x
G
E  arctan(Gy )
Gy  I Sy,
I is the image matrix
[0-360]
Sobel is derivative kernel which calculates the edges vertically and horizontally.

## Slide 8: Non-Maximum Suppression
Decode the Edge
Orientation
Comparison along
The edge orientation
Interpolation Value:
dTmp1, dTmp2
Neighboring Pixel Value:
g2, g4
Suppression: retain the
Local maximum
local maximum others
g  g
0

Non-maximum suppression is refinement of edges. It keeps information with high confidence and suppress the edges with low confidence.

## Slide 9: Edge Linking/ Edge Extension
l




tl  g  th weak edge=0.5
g  t non edge=0
Double Thresholding
(tl th )
g  th strong edge=1
Edge linking is the process of tracking the edge points and linking them to form an edge or boundary of an object in the image.

## Slide 10: Quality Assessment
 |  | Your Detection | 
 |  | T | F
Ground Truth | T | True Positive | False Negative
 | F | False Positive | True Negative
TPR  TP / (TP  FN )  correctly detected edge
FPR  FP / (FP  TN )  incorrectly detected edge
Accuracy  (TP  TN ) / (TP  TN +FP+FN)
Confusion Matrix

## Slide 11: Edge Detection Functions
Input Image: transfer image to gray format and pixel intensities to [0,1] range.
Gradient Computation: output gradient magnitude and direction at each pixel position.
Non-Maximum Suppression: output single-pixel-width edge image.
Double Thresholding: output pixel intensities should be 0, 0.5 or 1.
Edge Linking: output the final edge detection result.
Quality Assessment: output TPR, FPR.

## Slide 12: Optimization
Typically set th  2, tl 0.02
Initialize the parameter value. For example,  0.5, tl
Run the whole edge detection procedure on training images
Increase the parameter and repeat the procedure utill the best TPR, FPR or Accuracy is obtained
Test the optimized parameter set on the test image
Parameters: ( , th , tl )

## Slide 13: ROC Curve
Change Parameters and Plot TPR and FPR

## Slide 14: Discussion
Analysis of your detection results
Show some intermediate results
Describe and discuss about the optimization part
Any detailed or small step that makes a difference the detection performance (interpolation, edge linking, etc.)

## Slide 15: Marks Breakdown
+50 pts: Working implementation of Canny edge detector +30 pts: Working implementation of quality assessment and parameter optimization +20 pts: Writeup with several examples of hybrid images +10 pts: Extra credit (up to ten points) -5*n pts: Lose 5 points for every time you do not follow the instructions for the hand in format -5*n pts: Lose 5 points for every day you delay the submission of your report and codes beyond the due date.

## Slide 16: Data & Codes
Log onto eClass (https://eclass.yorku.ca/)
Choose the course 4690
Click into Canny Edge Detection and find the lab part

## Slide 17: Questions
Read the Lab2 introduction in detail
Email TA via maryumja@yorku.ca